## Slide 1
Step 2: Enter your location
Step 3: Click on this button
(Doing this will enter your longitude and latitude on the form for you).
Step 4: Click on the Calculate button
Step 1: Go to https://www.ngdc.noaa.gov/geomag/calculators/magcalc.shtml#igrfwmm

## Slide 2
Step 5: This calculated number tells you the downward component of the Earth’s magnetic field at your location in units of nano-Tesla (nT). Since you want the upward component in units of micro-Tesla (mT), you need to divide by -1000 to get BEz.
In this example BEz = 48553.8/(-1000) = -48.55 mT.
Your BEz value will probably be negative if you are in the northern hemisphere, and it will probably have a magnitude similar to the number shown. If you get something ten times bigger or smaller then you should make sure you didn’t make a mistake.

## Slide 3
Step 6: Put the BEz value that you found as described on the previous few pages into the Local Bz box on the Options and Preference panel.
Step 7: Restart your IOLab application and calibrate the magnetometer. Your new value of BEz will be used in the calibration.